## Slide 1: SIMD Processors (Vector Processing)
P. K. Roy
Asst. Professor
Siliguri Institute of Technology

## Slide 2: Problems with conventional approach
Limits to conventional exploitation of ILP: 1) pipelined clock rate: at some point, each increase in clock rate has corresponding CPI increase (branches, other hazards)
2) instruction fetch and decode: at some point, its hard to fetch and decode more instructions per clock cycle
3) cache hit rate: some long-running (scientific) programs have very large data sets accessed with poor locality; others have continuous data streams (multimedia) and hence poor locality

## Slide 3: Supercomputers
Fastest machine in world at given task
A device to turn a compute-bound problem into an I/O bound problem
Any machine costing $30M+
Any machine designed by Seymour Cray
CDC6600 (Cray, 1964) regarded as first supercomputer

## Slide 4: Supercomputer Applications
Typical application areas
  Military research (nuclear weapons, cryptography)
  Scientific research
  Weather forecasting
  Oil exploration
  Industrial design (car crash simulation)
All involve huge computations on large data sets
In 70s-80s, Supercomputer  Vector Machine

## Slide 5: Why Vector Processors?
A single vector instruction specifies a great deal of work—it is equivalent to executing an entire loop.
The computation of each result in the vector is independent of the computation of other results in the same vector and so hardware does not have to check for data hazards within a vector instruction.
Hardware need only check for data hazards between two vector instructions once per vector operand, not once for every element within the vectors.
Vector instructions that access memory have a known access pattern.
Because an entire loop is replaced by a vector instruction whose behavior is predetermined, control hazards that would normally arise from the loop branch are nonexistent.

## Slide 6: Vector Processing

## Slide 7: Vector Processor(1)

## Slide 8: Vector Processor(2)

## Slide 9: Vector Processor(3)
Self-Review : Vector instructions from Kai Hwang

## Slide 10: Vector Processor(4)

## Slide 11: Vector Architecture(1)
Basic idea:
  Read sets of data elements into “vector registers”
  Operate on those registers
  Disperse the results back into memory
Registers are controlled by compiler
  Register files act as compiler controlled buffers
  Used to hide memory latency
  Leverage memory bandwidth
Vector loads/stores deeply pipelined
  pay for memory latency once per vector ld/st!
Regular loads/stores
  pay for memory latency for each vector element

## Slide 12: Vector Architecture(2)

## Slide 13: Vector Unit

## Slide 14: Vector Unit Operation Model

## Slide 15: Vector Program

## Slide 16: Example: VMIPS
Vector registers
  Each register holds a 64-element, 64 bits/element vector
  Register file has 16 read ports and 8 write ports
Vector functional units
  Fully pipelined
  Data and control hazards are detected
Vector load-store unit
  Fully pipelined
  Words move between registers
  One word per clock cycle after initial latency
Scalar registers
  32 general-purpose registers
  32 floating-point registers

## Slide 17: Vector Chaining(1)
Vector version of register bypassing
Chaining
  Allows a vector operation to start as soon as the individual elements of its vector source operand become available
    Results from the first functional unit are forwarded to the second unit

## Slide 18: Vector Chaining(2)

## Slide 19: Vector Chaining(3)

## Slide 20: Advantages of Vector Processing
Each result is independent of previous results - allowing deep pipelines and high clock rates.
A single vector instruction performs a great deal of work - meaning less fetches and ewer branches (and in turn fewer mispredictions).
Vector instructions access memory a block at a time which allows memory latency to be amortized over many elements.
Vector instructions access memory with known patterns, which allows multiple memory banks to simultaneously supply operands.
Less memory access = faster processing time.

## Slide 21: Disvantages of Vector Processing
Not as fast with scalar instructions
Complexity of the multi-ported VRF
Difficulties implementing precise exceptions
High price of on-chip vector memory systems
Increased code complexity

## Slide 22: Array Processors

## Slide 23: Array processor(1)
A vector (one dimensional array)
A set of vectors (multi-dimensional array)
Array processor ─ a processor capable of processing array elements
Suitable for scientific computations involving two dimensional matrices
Array processor performs a single instruction in multiple execution units in the same clock cycle
The different execution units have same instruction using same set of vectors in the array

## Slide 24: Array processor(2)

## Slide 25: Array processor(3)

## Slide 26: Array processor(4)

## Slide 27: How Array Processor Can Help?

## Slide 28: How Array Processor Can Help?

## Slide 29: Classification

## Slide 30: Dedicated Memory Organization

## Slide 31: Global Memory Organization(1)

## Slide 32: Global Memory Organization(2)
Alignment/Interconnection

## Slide 33: Attached Array Processor

## Slide 34: ILLIAC IV

## Slide 35: ILLIAC IV Architecture

## Slide 36: References
PPT on Pipelining from CS303 (3rd Semester)
Advanced Computer Architecture – Kai Hwang
Advanced Computer Architectures – Dezso Sima, Peter Karsuk
Computer Organization – Carl Hamacher
Computer Architecture & Organization – John P. Hayes
Computer System Architecture – M. Morris Mano
Computer Organization & Architecture – T. K. Ghosh
Computer Organization & Architecture – Xpress Learning